## Slide 1
DeepStore: In-Storage Acceleration for Intelligent Queries
Vikram Sharma Mailthody, Zaid Qureshi, Weixin Liang, Ziyan Feng, Simon Garcia de Gonzalo, Youjie Li, Hubertus Franke*, Jinjun Xiong*, Jian Huang, Wen-mei Hwu
UIUC, *IBM Research
Notes: I have added the notes for you to read and understand what I had presented. The conference is not recorded but this notes should help you understand the details of the paper.
This work proposes an efficient system design for emerging deep learning based data queries.

## Slide 2
Value
Data Ocean
Intelligent Query
Key
Key
2
Notes: In the traditional database, we can build an efficient index with 1:1 mapping and a key can be used to easily get the desired value.
But these days, because of the development of machine learning, such a 1:1 mapping is not feasbile.
For example, I may want to search the data, say using a picture, and retrieve similar images with high accuracy.
For these types of workload it is very hard to build an index. This is because different intelligent queries require different semantic information about data,
and it is not possible to build a unified index that captures all the semantic information of data for all intelligent queries.
To help further understand this problem let me show you a concrete example of intelligent query

## Slide 3
Intelligent Query Example
Similarity
Comparison
Top K Images
Dataset
Intelligent
Query
{Owl on branch}
Similarity
Comparison
Network
3
Notes: Given a dataset and an image patch query, we would like to retrieve images similar to the query.
To do so, the query and each item in the dataset are first represented in an abstract format. This is then followed by a similarity comparison that generates a match score.
The resulting topk based on the match are then returned to the user.
Since the query is no longer restricted to be an image but can be of other forms such as audio, image, text or other, a deep learning based model is used for similarity comparison.
Deep learning models are proven to extract meaningful information from unstructured data which then can be used to do similarity comparison with high accuracy.

## Slide 4
State-of-the-art Intelligent Query System
Top K Images
Dataset
Intelligent
Query
{Owl on branch}
Similarity
Comparison
Network
Size = #images * size_of_feature_vector
Cannot Store in DRAM
+ Multiple applications
SSD
Offline
Comparison for all data items
Large execution time
What limits the performance?
4
Feature
vector DB
GPUs
Online
Notes: To support intelligent queries, state-of-art system use two phased approach. The first phase is the offline processing.
Offline phase involves extraction of feature vectors or embeddings for each item in the dataset and stored in the feature database.
Because we have large dataset and feature vector size is in few kbs, it is very hard to store the dataset in the DRAM and hence it is stored in SSDs.
In the online phase, a given query's feature vector is extracted using a model and then compared against database feature vectors using a SCN on GPUs.
Because these features are extracted using deep learning model, geometric properties such as Euclidian distance are not preserved, and we cannot build an index.
Hence, we have to generate a similarity score between the query and each item in the dataset. As a result, most of the time is spent on SCN computation.
So, we set out to understand what limits the performance of executing SCN.
Because we are trying to generate a similarity score between the query and each item in the dataset, most of the time is spent on SCN computation.
To make this worse, because we don’t have an index, we have scan the entire dataset.
After the offline processing, we support the online processing. Because we are trying to generate a similarity score between the query and each item in the dataset, most of the time is spent on SCN computation. To make this worse, because we don’t have an index, we have scan the entire dataset. “
In the online phase, a given query's feature vector is extracted using a model and
then used to compare with each database feature vector using a similarity comparison network to generate a match score.
Because we are trying to generate a similarity score, most of the time is spent on SCN computation.
To make this worse, because we don’t have an index, we have scan the entire dataset.
The state-of-art systems use GPUs/accelerators to perform these operations. Our profiling results showed that when executing an intelligent query,
query feature extraction takes a small portion of execution time as it occurs once, whereas the similarity comparison consumes most of the query time. So, we set out to understand what limits the performance of these SCN computations.
In the state-of-art system, Intelligent query execution works in two phases.
In the Offline phase, embedding vectors or feature vectors for each item in the dataset are extracted and stored.
Since the size of this feature vector db is proportional to number of features and the size of each feature vector, the db can be very large and thus the db is typically stored in SSDs. In the online phase, a given query's feature vector is extracted using a model and
then used to compare with each database feature vector using a similarity comparison network to generate a match score.
The state-of-art systems use GPUs/accelerators to perform these operations. Our profiling results showed that when executing an intelligent query,
query feature extraction takes a small portion of execution time as it occurs once, whereas the similarity comparison consumes most of the query time. So, we set out to understand what limits the performance of these SCN computations.
Speaking: spoke flatly. People did not feel excited. Each slide – what will you be delivering – to make this worse, we don’t index – we need to scan the entire dataset. – follow the clear logic - flat voice is not good – what is your insight and not what you have done.

## Slide 5
Intelligent Query Workload Characterization
+
Platform
Person Reidentification (ReID)
Music Information Retrieval (MIR)
Exact Street to Shop (ESTP)
Text-2-Image Retrieval (TIR)
Text Q&A (TextQA)
+
NVMe SSD
VOLTA
PASCAL
5
Notes: We characterized the performance of intelligent query workloads spanning 3 different domains: visual, audio, and text.
We use a platform with 2 different generations of high-end GPUs: Pascal and Volta, a low latency high thoughtput NVMe SSD, and the Tensorflow framework.
This represents the state-of-art system for executing intelligent queries.

## Slide 6
Chart: Time in %
| Pascal | Volta | Pascal | Volta | Pascal | Volta | Pascal | Volta | Pascal | Volta | ReID | MIR | ESTP | TIR | TextQA
Compute | 196.21 | 131.64 | 7.13 | 6.58 | 22.56 | 20.58 | 3.93 | 3.43 | 4.68 | 3.4
CPU2GPUTx | 7.79 | 7.79 | 8.505 | 8.505 | 67.675 | 67.935 | 8.47 | 8.52 | 9.068 | 9.067
SSD IO | 114.87 | 179.4402 | 160.297 | 160.847 | 1397.48 | 1397.48 | 189.605 | 190.055 | 124.202 | 124.202
Intelligent Query Workload Characterization
SSD IO Time: ~56-90% in Volta
Intelligent Query performance is limited by SSD I/O bandwidth
6
Notes: To further understand these IQ workloads, we breakdown the total query execution time into three stages.
The first stage is the GPU computation time, the second is the time spent to load data from host memory to GPU memory and third is the time spent to load data from SSD.
We find that the SSD IO is the bottleneck. Even with the newer generation of high-end GPU, Volta, we cannot see performance improvement because the storage IO is the bottleneck.
Trashed:
Here we show the different applications with the 2 generations of GPUs on the x-axis The y axis represents the breakdown of the query execution time. As you can see from figure, GPU computation constitutes on a small fraction of the total time. Further the newer generation GPU, Volta, improves that time by 20%. Transferring data from the CPU memory to the GPU is only a small fraction of total time. Majority of the time is spent in reading the data from the SSD due to the limited IO bandwidth. As shown here, this constitutes upto 90% of the time when using the Volta GPU. Thus, the performance of these workload is bottlenecked by the SSD IO bandwidth, this bottleneck will only worsen with the introduction of accelerators.

## Slide 7
Design In-Storage Accelerators
Intelligent Queries Study Results
Similarity comparison networks require high-throughput computation
Intelligent Query performance is limited by SSD I/O bandwidth
Move Computation to Storage
Data Ocean
SSD I/O
bandwidth
7
Notes: To recap, IQ perf is limited by SSD IO bandwidth.
To address this, we can move the computation to the SSD. In-storage computing is not a new concept. However, enabling in-storage computing to support these IQ workloads is a challenge
Because, wimpy cores in the SSD cannot efficiently support complex operations such FC and convd layers present in SCN
And resources in the SSD are limited.
To address this, we design in-storage programmable accelerators for intelligent queries.

## Slide 8
DeepStore Accelerator
Rectangular
Systolic Array
Scratchpad
Accelerator Controller
Flash Controller
Flash Plane
Flash Plane
Flash Plane
Flash Plane
Page Buffer
Flash Chips
Queue
DeepStore Accelerator
SCN
Weights
Inputs
Outputs
Outputs
QFV
Weights
DFV
QFV: Query Feature Vector DFV: Dataset Feature Vector SCN: Similarity Comparison Network
8
Notes: “Now lets do a deep dive to discuss how the in-storage accelerator in DeepStore looks like.
Because the accelerator is used to speedup the SCN computation, that mainly constitutes of FC layers, we use a rectangular systolic array of PEs.
The systolic array is coupled with a scratchpad and a controller, as shown here. The accelerator controller is an FSM responsible for keeping track of computation and data movement.
There is another challenge, the accelerator needs to fetch the dataset feature vectors from the flash chips.
Thus we need to build a mechanism between the flash chips and the accelerator for data transfer.
In our scheme, the accelerator controller interacts with the flash controller to read input flash pages from the flash planes. These flash pages are then queued up before they are loaded into the scratchpad. The systolic array uses the inputs from the scratchpad to perform the SCN computation.
This design decouples the SCN execution in the systolic array and reading of inputs from flash.
So far we have shown how DeepStore exploits the compute parallelism present in SCN computation. To further ….

## Slide 9
SSD controller/firmware
Internal bus
Embedded
cores
DRAM
Block I/O Interface
Flash
Channel - 0
Channel - 1
Channel - 2
Channel - N
Query
Interface
SSD
DeepStore: In-storage Acceleration for Intelligent Queries
Channel
-
0
Flash
Flash
Flash
Flash
Channel
-
1
Flash
Flash
Flash
Flash
Channel
-
2
Flash
Flash
Flash
Flash
Channel
-
N
Flash
Flash
Flash
Flash
9
DeepStore
SSD Acc
Channel
Acc
-
0
Channel
Acc
-
1
Channel
Acc
-
2
Channel
Acc
-
N
Chip level accelerators
Notes: To further improve the performance, we can exploit the parallelism provided by the SSD.
For those who may not know the internal architecture of an SSD, SSDs offer 3 levels of parallelism – ssdlevel, channel level and chip level.
This means, we have 3 choices to place the accelerators: (1) at the SSD level, (2) at the channel and lastly at the chip level.
To find which one is better it is important to understand the trade off of placing the accelerator at each level to gain the maximum performance.

## Slide 10
Challenges for DeepStore Design
Limited Power Budget
Limited SSD DRAM Bandwidth
SSD Level | 55W | 25.6GBps
Channel Level | 55W / 32 | 25.6GBps / 32
Chip Level | 55W / 128 | 25.6GBps / 128
Design Space Exploration
SSD Level | 32x64 PEs, 8MB Scratchpad
Channel Level | 16x32 PEs, 8MB Scratchpad (shared), 512KB RegFile
Chip Level | 4x32 PEs, 8MB Scratchpad (shared), 512KB RegFile
10
Notes: Because of the power budget and DRAM bandwidth limitation in the SSD, the number of PEs and scratchpad size are constrained differently at each level.
The ssd level accelerator would have access to entire power budget and bandwidth.
However, for the channel and chip level designs, the accelerators have to share the power budget and bandwidth.
Based on these design constraints for each level of accelerator, we perform design space exploration to arrive at the following optimal design points for each accelerators. Please read the paper for further details

## Slide 11
Performance Comparison Against SSDLevel Accelerator
11
Chart: Speed Up
| ReID | MIR | ESTP | TIR | TextQA
Wimpy Cores
SSDLevel | 1 | 1 | 1 | 1 | 1
ChannelLevel | 43.5556 | 25.8125 | 22.3051 | 24.2727 | 44.35
ChipLevel | 3.1562 | 3.2203 | 3.3409 | 11.55
DeepStore's channel level design performs best as it provides the best tradeoff between the parallelism exploited and per-accelerator compute capability.
Failed to execute
Notes: We further evaluate the performance of each design using the applications previously discussed.
The applications are on the x-axis and the y shows the speed up compared against the SSDLevel accelerator.
Even though chip level design exploits the most parallelism, its performance is lower than the channel level accelerator because each of the chip level accelerators have limited compute resources at its disposal.
Overall, the channel level design performs the best as it provides the best tradeoff between parallelism exploited and per-accelerator compute capability.

## Slide 12
SSD controller/firmware
Internal bus
Embedded Cores
DRAM
Block I/O Interface
Channel - 0
Channel - 1
Channel - 2
Channel - N
Query interface
DeepStore
Acc
Acc
Acc
Acc
DeepStore Runtime System
loadModel(cg, cg_size)
Query
engine
SCN Model
query(qfv, model_id, …)
QFV
QFV
QFV
QFV
QFV
writeDB(…)
Multiple apps (dbs)
 striped across channel/chips
db1
db2
Each DB has a metadata persisted in reserved Flash block
1
0x00AEB00
0x1000
2048
2
0x1DE3200
0xF1000
8196
dbID
start_phyAddr
#features
#fsize
QFV: Query Feature Vector SCN: Similarity Comparison Network
12
Notes: So far, based on the design space exploration, we placed the accelerator in the channel level.
Now to make DeepStore practical, we build a runtime system that can handle multiple SCN models and feature databases.
The runtime system or the query engine is a software running in the embedded processors, manages the query execution
and provides required APIs for the user to program DeepStore. The loadModel API, allows loading a user-defined SCN model to the SSD DRAM.
The query API transfers the QFV features to the QE which forwards it along with the SCN model and other metadata to accelerators to perform IQ execution.
The writeDB API allows the user to write a feature vector database to the SSD. It ensures that the DBs are page, plane, chip, channel aligned so the accelerators can read them correctly. For each database, we store metadata in reserved Flash blocks. During IQ execution, accelerators use this metadata to generate addresses for feature vectors.
Thus the query engine enables DeepStore to support multiple different databases and SCN models.

## Slide 13
DeepStore Query Cache
Optimization: exploit temporal locality and semantic similarity of queries
Q1. A brown dog is running in the sand
DeepStore SSD
Query Engine
Feature Vector DB
Q1
SCN
TopK
Q2. A brown dog plays at the beach
Semantically similar query
Q2
SCN
Q1TopK
Query Engine
Query Cache
13
QFV: Query Feature Vector SCN: Similarity Comparison Network
Notes: To further improve the performance of DeepStore, we also have an interesting cache design – based on the insight that intelligent queries can exhibit semantic similarity.
So far when we get a query, we perform SCN computation across the database and respond with topK results.
Now if a similar query arrives, and if we could determine it is semantically similar to a previous query,
instead of computing SCN over the db again, we could send the previously computed results to the user.
To do this, we add a software query cache to the DeepStore query engine.

## Slide 14
QFV: Query Feature Vector QCN: Query Comparison Network
DeepStore Query Cache Workflow
1
QC_QFV
Top1, Top2…
1
QB_QFV
Top1, Top2…
...
…
…
...
…
…
Valid
QFV(Tag)
TopKFV
Q2_QFV
Query Cache
QCN
QA_QFV
ScoreQA
QB_QFV
QC_QFV
ScoreQB
ScoreQC
Hit
14
Notes: Each entry in the Query Cache has a valid bit, a tag, which is the previously executed query feature vector, and the topk results of that previously executed query as data.
Unlike a regular cache, the query cache uses a neural network model to determine hits and misses. When a new query arrives, it checks if the query is semantically similar to any QFV in the cache using a query comparison network.
The maximum score is then picked and compared against a programmable threshold to determine if it’s a hit or miss.
If its a hit, then the results from the cache are returned.

## Slide 15
SSD controller/firmware
Internal bus
Embedded
cores
DRAM
Block I/O Interface
Query
engine
Channel
Acc
-
0
Channel
Acc
-
1
Channel
Acc
-
2
Channel
Acc
-
N
Channel - 0
Channel - 1
Channel - 2
Channel - N
DeepStore
Putting It All Together
QFV
Query Cache
SCN Model
QFV: Query Feature Vector
QFV
QFV
QFV
QFV
SCN
SCN
SCN
SCN
TopK
TopK
TopK
TopK
Hit
Miss
SCN Model
Query
Interface
TopK
TopK
15
Notes: Now lets put everything together and let me show how DeepStore works. At the beginning, the SCN models are loaded to the SSD DRAM using the DeepStore API. During a query, the QFV is extracted and sent to the query engine which determines if it’s a hit or miss in the query cache.
If hit, the cached topk results are sent out.
If miss, the SCN computation is performed using the DeepStore accelerators.
Each accelerator is going to generate local topK results which are later merged to generate final topK results to be sent out as a response.

## Slide 16
Experimental Setup
Comparison
Volta GPU+SSD System (Traditional)
SSD Wimpy cores (8-core A57 ARM)
Channel-level accelerator design (DeepStore)
Workloads
Visual
  Person Reidentification (ReID)
  Exact Street to Shop (ESTP)
Audio
  Music Information Retrieval (MIR)
Text
  Text-based Image Retrieval (TIR)
  Question and Answer (TextQA)
16
Notes: To evaluate the efficiency of DeepStore we compare with the traditional GPU + SSD system and with the wimpy processors present inside the SSD.
We use Volta GPU in the baseline and for the wimpy cores – we use a 8-core A57 ARM CPU running at 2GHz.
We use 3 types of workloads and with a 500GB dataset.
We first evaluate the performance and energy efficiency benefits of DeepStore without the query cache enabled.

## Slide 17
Chart: Speed Up
Traditonal | 1 | 1 | 1 | 1 | 1
Wimpy Cores | 0.004 | 0.0203 | 0.0358 | 0.02778 | 0.0882
SSDLevel
DeepStore | 3.92 | 8.26 | 13.16 | 10.68 | 17.74
ChipLevel
Performance Benefit of DeepStore
DeepStore performs up to 17x faster due to the removal of I/O bottleneck, parallelism exploited, and high reuse of weights
17
0.004
Notes: First we evaluate DeepStore's performance benefit when compared against the traditional system and wimpy cores. Here we show the applications on the x axis and the speed up over the traditional system on the y axis. As expected, Wimpy cores are significantly slower than the baseline as they are inefficient in executing deep learning models.
On the other hand DeepStore performs upto 17x faster than the traditional system due to the removal of the IO bottleneck, level of internal parallelism exploited, and the high reuse of model weights.

## Slide 18
Chart: Relative Enegry Efficiency
Traditional | 1 | 1 | 1 | 1 | 1
Wimpy Cores | 0.00051356 | 0.0015903 | 0.0020319 | 0.001708 | 0.0024542
SSDLevel
DeepStore | 17.1071 | 27.9169 | 38.5789 | 35.5869 | 78.6044
ChipLevel
Energy Efficiency Benefit of DeepStore
DeepStore is up to 78x more efficient than GPU for intelligent queries
18
Notes: Next we evaluate the efficiency of the DeepStore.
We use performance per watt as the metric and compare DeepStore with the traditional system and wimpy cores across the different applications.
Although the wimpy cores consume less power than the GPU system, they are not nearly as performant.
Thus their efficiency is significantly lower than the traditional system.
However, DeepStore is not only faster than the traditional system but also 4 times more energy efficient, as it reduces power consumed for data movement.
Thus, DeepStore improves perf/watt by 78x.

## Slide 19
Chart: Match Threshold
| 1 | 0.98 | 0.95 | 0.92 | 0.9 | 0.88 | 0.85 | 0.82 | 0.8
Traditional + Qcache | 1.32 | 1.779 | 1.783 | 1.7956 | 1.811 | 1.8385 | 1.9294 | 2.133 | 2.357
Miss Rate | 75.77 | 56.21 | 56.07 | 55.69 | 55.21 | 54.39 | 51.83 | 46.88 | 42.43
Query Cache Performance
Query Cache in DeepStore can significantly improve
performance due to DeepStore's lower miss penalty
19
Chart: Match Threshold
| 1 | 0.98 | 0.95 | 0.92 | 0.9 | 0.88 | 0.85 | 0.82 | 0.8
Traditional + Qcache | 1.32 | 1.779 | 1.783 | 1.7956 | 1.811 | 1.8385 | 1.9294 | 2.133 | 2.357
DeepStore | 11.852 | 11.852 | 11.852 | 11.852 | 11.852 | 11.852 | 11.852 | 11.852 | 11.852
DeepStore + Qcache | 15.354 | 20.1635 | 20.209 | 20.3328 | 20.492 | 20.769 | 21.6845 | 23.7055 | 25.873
Miss Rate | 75.77 | 56.21 | 56.07 | 55.69 | 55.21 | 54.39 | 51.83 | 46.88 | 42.43
Notes: We now enable query cache and pick the Text2Image Retrieval (TIR) application to determine the performance benefit. We use a dataset of 100M Images and 100K Queries and sample the queries using a power-law distribution . The x axis shows the impact of relaxing the threshold for determining a cache hit.
The left y axis shows the relative performance improvement of each system over the traditional GPU+SSD system where as the right y axis shows the miss rate of the QC.
We first show the performance improvement of adding the QC to the traditional system. The performance of the traditional system is improved due to the lower miss rate.
However, the traditional system with the query cache is still slower than DeepStore without the query cache. When we add the query cache to DeepStore, it improves DeepStore's performance by upto 26 times over the traditional system, due to DeepStore's lower miss penalty.

## Slide 20
DeepStore
Summary
DeepStore
SSD Controller
Channel
Channel
Channel
20
Channel
Notes: To summarize, with the development of machine learning workloads, we believe intelligent queries will be the next generation workload.
We develop in-storage accelerator for efficient execution of Intelligent queries and we find that it is feasible.
Compared with the traditional GPU+SSD system and wimpy cores, DeepStore’s channel level design is both performant and energy efficient.
Thank you and we are happy to take any questions.

## Slide 21
Thank you!
21